## Slide 1: Time in Networking
A microsecond is one millionth of a second.
1 microsecond = 1µs = 0.000001 sec = 1 x 10-6 sec
A millisecond is one thousandth of a second.
1 millisecond = 1 ms = 0.001 sec = 1 x 10-3 sec

## Slide 2: Size in Networking
A kilobit is one thousand bits.
  1 kb = 1 x 103 = 1,000 bits
  (In the context of storage-memory and address-space sizes, the alternative binary definition is 1 kb = 210 = 1,024 bits.)
A megabit is one million bits.
  1 mb = 1 x 106 = 1,000,000 bits
  (In the context of storage-memory and address-space sizes, the alternative binary definition is 1 mb = 220 = 1,048,576 bits.)
Note the above are in bits
  Byte, usually abbreviated with a capital ‘B,’ is usually equal to 8 bits.

## Slide 3: Packet Switching
Applications exchange messages broken into pieces called packets
  No path or link is reserved
  More like the postal system
  Packet sent by users “take turns” using resources

## Slide 4: Network Core: Packet Switching
Packets are routed through a series of links from the source to destination
  Routed between links by packet switches or routers
  Packets are transmitted at full link bandwidth
  Store and forward: packets normally move one hop at a time
    Each node must receive the entire packet before forwarding
    Incoming packets are stored in a buffer till processed
  Aggregate resource demand by network users can exceed amount available
    Congestion: packets queue, wait for link use

## Slide 5: Network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 6: Alternative Network Core
There are two primary paradigms for routing data and information through a network
  Circuit switching (i.e. telephone networks)
  Packet switching (i.e. computer networks)

## Slide 7: Network Core: Circuit Switching
Resources needed along the communication path are reserved
  Reserved resources to make up an end-to-end connection constitute a circuit
  Each connection or “circuit” gets 1/nth of the link bandwidth

## Slide 8: Network Core: Circuit Switching
Characteristics:
  Constant transmission rate
  Guaranteed throughput
  Resources associated with the circuit wasted when no data is being transmitted
  Each link is broken into n circuits capable of supporting a single connection.
  Different Methods of dividing link bandwidth into “pieces”
  frequency division
  time division
  code division

## Slide 9: Circuit vs. Packet Switching
Packet switched networks can handle more users if the users are not continuously transmitting
  Packet switching is entirely based on this assumption
Suppose the following…
  Link Characteristics:
    1 Mbps bandwidth
  User Characteristics:
    100 kbs when transmitting
    Transmitting 10% of the time
N users
1 Mbps link

## Slide 10: Circuit vs. Packet Switching Continued
Circuit Switching:
  Total bandwidth divided by number of users
  Maximum of ten users
  Can only transmit at 1 Mbps/10
Packet Switched
  With 35 users less than .0004 probability more 10 are active at any moment
  Can transmit at 1 Mbps

## Slide 11: Packet switching versus circuit switching
great for bursty data
  resource sharing
  simpler, no call setup
excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem
Is packet switching a “slam dunk winner?”

## Slide 12: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
Q: how did we get value 0.0004?
Q: what happens if > 35 users ?
…..
* Check out the online interactive exercises for more examples

## Slide 13: Four sources of packet delay
  Sum of delays for a single node is the total nodal delay
  Sum of delays for entire path is end-to-end delay (Sum of all nodal delays)
A
B
propagation
transmission
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop

## Slide 14: Nodal Processing Delay
Time needed for the router to examine the packet and decide what to do with it
Depends on processing speed of the node
  Check bit errors
  Determine which output link
Microseconds or less

## Slide 15: Nodal Transmission Delay
Time required to push bits into an output link
Depends on bandwidth of the output link and size of the packet
  R = link bandwidth (bps)
  L = packet length (bits)
  Transmission Delay = L/R
Microseconds to milliseconds

## Slide 16: Propagation Delay
Time required for the bits to travel the length of the link
  Depends on type of transmission medium and length of the link
  d = length of physical link
  s = propagation speed in medium (~2.5x108 m/sec)
  Propagation Delay = d/s
  Different physical media have different propagation speeds
  Milliseconds in wide area networks

## Slide 17: Transmission Delay versus Propagation Delay
Transmission delay is a function of:
  Bandwidth
  Packet size
Propagation is a function of:
  Link length
  Propagation speed
http://media.pearsoncmg.com/aw/aw_kurose_network_2/applets/transmission/delay.html

## Slide 18: Nodal Queuing Delay
Packets queue at a node when arrival rate exceeds output capacity
  Depends on congestion level of network
  Time waiting at output link for transmission
  Modeled as a random process
  Varies from packet to packet
  Depends on how many packets are in the input queue when a packet arrives at a node
  If the number of queued packets exceeds buffer capacity, packets are dropped or lost
Microseconds to milliseconds to infinity

## Slide 19: Nodal vs. End-to-End Delay
Total Nodal Delay
  Delay for a single node or router
  dnodal = dproc + dqueue + dtrans + dprop
End-to-End Delay
  Simple delay from source to destination
    Assume there are N - 1 routers between a source and destination
    Assume uncongested network (no queueing delay)
    Assume homogenous nodes and links
dend-end = N (dproc + dtrans + dprop)

## Slide 20: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 21: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, 1st car arrives at second booth; three cars still at 1st booth.
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 22: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 23: Traffic Intensity
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
* Check out the Java applet for an interactive animation on queuing and loss
traffic intensity = La/R

## Slide 24: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 25: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org

## Slide 26: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 27: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 28: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 29: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 30
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 31: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols

## Slide 32: Protocols
  A protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of a message or other event.
  Communication between two entities is normally governed by a protocol.
    Numerous types with different goals
    One protocol may be built on top of or use another protocol.
    In computers, protocols may be software or hardware implemented.

## Slide 33: Protocol Layers and Stacks
Object oriented programming breaks complex programs into manageable smaller pieces.
Likewise, software and firmware supporting network communication is broken into protocol layers.
  Each layer only communicates with the layers immediately above and below
  Generically the layers pass protocol data units (PDUs) up and down the stack
  Modularization eases maintenance, updating of system
  Change of implementation of layer’s service transparent to rest of system (Encapsulation)

## Slide 34: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 35: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 36: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 37: Internet Protocol Stack (Application Layer)
Application: content of messages applications send
  It is the data
    Has nothing to do with getting from source to destination
  Example Protocols: FTP, SMTP, STTP, HTTP
  Software implemented
  Chapter 2

## Slide 38: Internet Protocol Stack (Transport)
Transport: host application to host application segment transfer
  Only runs on end systems
    Organizes and keeps track of message pieces
  Protocols: TCP, UDP
  Links application to the network
  Software implemented
  Chapter 3

## Slide 39: Internet Protocol Stack (Network Layer)
Network: routing of datagrams from source to destination
  Determines next computer based on destination
  Internet routing protocol: IP
  Mixed implementation of hardware and software
  Chapter 4

## Slide 40: Internet Protocol Stack (Link Layer)
Link: frame transfer between neighboring network elements
  Groups bits together
  Protocols: PPP, Ethernet
  Implemented in network interface card
  Chapter 5

## Slide 41: Internet Protocol Stack (Physical Layer)
Physical: move individual bits “on the wire”
  Defines what constitutes a bit
  Implemented in network interface card
  Includes all hardware devices

## Slide 42: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 43: Chapter 1: roadmap
  1.6 networks under attack: security
Notes: 43

## Slide 44: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 45: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 46
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Bad guys: attack server, network infrastructure

## Slide 47: Bad guys can sniff packets
packet “sniffing”:
  broadcast media (shared ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  wireshark software used for end-of-chapter labs is a (free) packet-sniffer

## Slide 48: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B dest:A payload
… lots more on security (throughout, Chapter 8)

## Slide 49: Packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 50: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 51: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up